Requirements:
- Overview
-Project description
-Design relevance
-Goals, objectives and constraints
- Methodology
-Languages
-Development and collaboration tools
- Architecture
-System, data, and program design
- Testing
-Types and purpose of testing
-Performance constraints
- Team Roles
- Design Cohesion

This is a reformatted structure to abide by the above requirements.
Zach – I'm going through each section and appending more information.

 1 Introduction
2.1 Document intent
This design document serves as a reference, outlining all information pertaining to the
Punnet of Berries project. It is intended to provide an overview of design
considerations and technical specifications regarding the final implementation.
Descriptions of system design will be shown to allow for the understanding of what
is to be constructed and how it will be built.
This document should not be considered an installation or configuration guide; its
primary goal is to detail the design, development, and functionality of the cluster.

2.2 Document overview
Outlined in this document is the framework on which the Punnet and its accompanying
software were developed. Each iteration in the development process is illustrated in	detail in each section, covering system design, architecture, and implementation.
Within this are accompanying graphical documentation and requirement specifications
to aid in the understanding of system architecture.

2.3 Scope
The breadth of A Punnet of Berries has been intentionally delimited in order to make it
it feasible in a relatively short period of time. Given the allocated time span in which
development has been defined, it is important to delineate any milestones that need to be
achieved in the early alpha phase of design. This will be covered in 2.2 Goals and	Objectives.
This design document is focused on core architectural design and critical parts of the
system. As the project incorporates many pre-existing systems in conjunction with
custom software, a large focus will be attributed to the interaction of these components.

2.4 Methodology & Tools
Given the collaborative effort of the development process, it is prudent to
define best practices and design principles to abide by. All protocols must adhere to a
certain standard to promote scalability and ease of use.
Our design approach is one that highlights the employment of parallel processing,
concurrency, and synchronization. Fundamental operating system concepts will be
explored and integrated, exposing the Raspberry Pi as a viable platform for cluster
computing as well as comprehension of underlying technologies.

Design Principles:
-Scalability
-A computer cluster is by its nature designed to be scalable. This inherent
design characteristic must be adhered to, avoiding any sort of strict node
limitations.
-Usability
-As this project is largely for educational purposes, the cluster should
be easily constructed with high cohesion. The final application interface
should also be readily accessible.
-Flexibility
-The software should be customizable, allowing users to specialize;
secondary choices should be made available to enhance the application.

2 Design Overview
2.1 Vision
The final incarnation of a Punnet of Berries is ideally a financially viable Beowulf	cluster that draws minimal power and demonstrates the power of parallel computing.
This will be achieved with the utilization of inexpensive hardware and open source	technologies to adhere to time and design constraints. In order for the aforementioned
project to function properly, resources will need to be managed and allocate by a batch
scheduler. The Punnet of Berries will be accompanied by a custom batch system, the	Berry Batch.

2.2 Goals and Objectives
The immediate goal of this project is to implement a full functional Beowulf cluster that
is capable of demonstrating the performance advantages of parallel computing. Keeping
in mind these milestones are dynamic in nature as the development cycle progresses.
These objectives will become exhaustive over time and will be presented in such a way
as to indicate project priorities and design principles to abide by.

Priority Objectives:
-Establish open source tools that will be utilized.
-Generate system topology and determine appropriate interfaces.
-Develop system and application design.
-Determine most appropriate software development methodology.

2.3 Functional & Non-functional Requirements
Functional Requirements:

Non-functional Requirements:
-Scalability
-Testability
-Reliability
-Documentation
-Open Source

2.3 Constraints & Limitations

Hardware: Raspberry Pi
Given the Raspberry Pi is a comparatively low end single-board computer, we have
to make sure the design process accommodates for these hardware specifications.
The Pi platform houses a SoC (System on a Chip) Broadcom BCM2835; this includes
the 700 MHz ARM core, a VideoCore IV GPU, and 512 MB of SDRAM. As the
Pi does not feature any sort of non-volatile storage aside from an SD card, efficiency is
a concern when constrained to a low capacity memory card. There also exists a sort of
bottleneck in the interfaces (USB and Ethernet) as they both share the same bandwidth.
An additional concern is of power distribution in regards to scalability; this would likely	be resolved with the utilization of custom power supplies, but nonetheless it is	something to consider.

Hardware: Scalability
Despite having only limited resources (strict number of Raspberry nodes), it is
critical that our design approaches performing tasks in a unified manner. The overall
topology should be abstracted to the end user, permitting those with minimal technical	familiarity to still utilize the cluster effectively. This design constraint largely focuses on
the deployment of functioning, scalable cluster software. Ideally the user would just
specify the number of nodes in the cluster to run any particular job.

Software: Parallelism and Concurrency
An immediate area of concern is the difficulty in developing software that executes
computations in a parallel manner by distributing them across multiple cores. The
Raspberry Pi shouldn't be considered as an option for high-performance cluster
computing relative to desktop deployments. Rather, it is more a demonstration
of distributed computing for educational purposes.

Software: Architectural Considerations and Code Compilation
Raspberry Pi hosts a single-core ARM processor, operating at 700MHz (with
overclocking available). Due to this, any software developed in languages that are
high-level, architecturally dependent will need to be recompiled on the Pi itself.

2.4 Intended Process
Due to the unforeseeable nature of collaborative development, our team is more
inclined to adopt a sort of cyclic waterfall model. This methodology allows us
to clearly define phases of development to chart progress and fulfill milestones.
Such an iterative approach facilitates backtracking, which is beneficial considering
the scope of the project.

2.5 Process
Chronological list of tasks; define milestones here.

2.6 Design Forecast & Potential Issues
This project forecast will expand as more advancements are made in development.
Each stage of the waterfall method presents unique unforeseeable issues that
can only be documented when they arise.

Requirements Stage:
Design Stage:
Construction Stage:
Integration Stage:
Testing Stage:
Installation:
Maintenance:

3 System Overview
3.1 System Information

3.2 Topology

3.3 Hardware & Software Specifications

3.4 System Functions

4 Architecture
4.1 System Architecture

4.2 Program Architecture

4.3 Application Implementation & Integration

5 Testing
5.1 Compute Cluster

5.2 Batch System Tests

6 Roles and Responsibilities